## Slide 1
07/30/26
Dr. Adnan Jaran
<number>
بسم الله الرحمن الرحيم
Al-Imam Mohammed Bin Saud University
College of Medicine

## Slide 2: PRINCIPLES OF DISEASE I BLOCK (PATH 111) Credit Hours: 5 (2+2+1)
MICROBIOLOGY
Adnan S. Jaran BSc. MSc. PhD. AIBMS.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 3: Specimen collection and transport for identification of infectious diseases
07/30/26
Dr. Adnan Jaran
<number>

## Slide 4: Objectives
Know the general principle of specimen collection
Know considerations for specimen collection
Know the proper ways to transport specimen
Know specific methods for collecting Urine, Respiratory Sputum, Blood culture, CSF and other sterile body fluids and Stool for C. difficile. Samples for microbiological cultures.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 5: Collection & transposition of Specimen
Collection & transportation of Good quality specimen for microbiological examination is crucial

## Slide 6: GENERAL PRINCIPLE
Proper collection and transport of specimens is critical to the quality of results produced by the microbiology laboratory.
The validity of all diagnostic information produced in the lab is contingent on the quality of the specimen received.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 7
Consequences of poorly collected and/or poorly transported specimens include failure to isolate the causative organism, and recovery of contaminants or normal flora which could lead to improper treatment of the patient.
The saying is "garbage in--garbage out." The importance of proper collection of specimens cannot be over emphasized.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 8: GENERAL CONSIDERATIONS
A. Safety
1. Follow universal precaution guidelines in obtaining specimens for culture.
2. Do not contaminate the external surface of the collection container and/or any accompanying paperwork with the material being collected.
3. Minimize direct handling of specimens in transit by using plastic sealable bags, labeled with a biohazard label, with a separate pouch for the lab paperwork.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 9
B. Patient Identification
1. The patient is provided a computer generated armband at the time of admission that contains name, account number, permanent medical record number, date of birth, age, sex, social security number, room number, and attending physician.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 10
2. Personnel responsible for specimen collection checks armband information against request for test using name and DOB as the two patient identifiers, before specimen is collected.
3. In the case of outpatients, no armband is available. Collection personnel asks patient to identify themselves by name and date of birth.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 11
C. Patient Preparation and Instruction
1. For specimen collection in which the patient is responsible and unsupervised, verbal and/or written instructions are given to the patient at the time specimen containers are issued (i.e. - stool collection instructions).
07/30/26
Dr. Adnan Jaran
<number>

## Slide 12
D. Collection
1. Collect specimen before administration of antimicrobial agents when possible.
2. Collect a sufficient quantity of specimen. Too little may yield false negative results.
3. Collect with as little contamination from normal flora as possible to ensure that the specimen represents the infected site. If collection is through intact skin, cleanse the skin first.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 13
4. Collect specimens at the most active stage of the disease to increase chances of isolation and identification of the causative organisms. Sample the body area, lesion, exudate, or drainage most likely to contain the suspected pathogen (i.e., the leading edge of a skin lesion; depth of a wound, not the surface; sputum, not saliva).
07/30/26
Dr. Adnan Jaran
<number>

## Slide 14
5. Use appropriate collection devices, sterile equipment, and aseptic technique. Use only the standard equipment recommended by the laboratory. Do not substitute makeshift containers, bottles, or tubes.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 15: Urine Specimen
Sterile Urine container

## Slide 16: Stool Specimen

## Slide 17: Stool specimen

## Slide 18: Labeling of Specimen
1. The specimen must be identified with:
a. Patient name and Date of Birth (this must be on each specimen)
b. Identification number
c. Source or Clinical Diagnosis
d. Date
e. Time of collection
2. Identify the source correctly and specifically, so proper collection media will be selected during processing by the laboratory. ("Wound" is not an acceptable identification of a source. "Right lower leg incision" is a better example of adequate identification.)
07/30/26
Dr. Adnan Jaran
<number>

## Slide 19: Transport
All specimens should be transported in the appropriate medium for the source. Take care to ensure the specimen makes good contact with the medium (i.e., Shake well; squeeze the sponge to moisten the swab of an aerobic culturette; push the swab cap of the anaerobic culturette all the way down to the rubber stopper).
07/30/26
Dr. Adnan Jaran
<number>

## Slide 20
Transport all specimens to the laboratory promptly (within 30 minutes of collection). Specimens submitted without preservative (i.e., aspirate in a syringe) must be transported immediately and hand delivered to the microbiology tech on duty.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 21: Rapid transport
a. Ensures the survival and isolation of fastidious organisms and prevents overgrowth by more hardy bacteria.
b. Shortens the duration of specimen contact with any local anesthetics used in collection that might have antibacterial activity.
c. Provides a more accurate assessment of the number of organisms present in the infectious disease process.
All specimens for culture must be transported in a suitable container or placed in a biohazard bag for safe transport to the laboratory.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 22: Setting the scene
Issues in Microbiology
Brief overview
  Urine
  Respiratory Sputum
  Blood culture
  CSF and other sterile body fluids
  Stool for C.difficile

## Slide 23: Specimen collections
Samples are often collected by the nurses; doctors are responsible for initiating treatment
Lack of knowledge that
  Body is colonised with microbial flora and ‘pathogen’ can be found as a part of normal colonizing flora
  Unable to differentiate between ‘colonisation’ and infection
  Often positive ‘Bacteriology culture report’ is treated then patients
  As a result inappropriate/excessive antibiotics are prescribed

## Slide 24: MICROBIOLOGY
Information derived from the results has impact on :
  Diagnosis of infectious diseases
  Antibiotic prescribing
  Formulation of local antibiotic policy
  Public health impact eg food handlers
  Infection Control measures eg MRSA,
  PfA target for reduction of C difficile, MSSA and MRSA bacteraemias

## Slide 25: Urine
Mid Stream Specimen of Urine (MSSU)
Transport system: Sterile urine container
Specimen volume:
        -Bacteria 1ml
        - Mycoplasma > 10ml
Contamination of specimen with bacteria from urethra and vagina should be avoided.(HOW?),
first voided portion is discarded.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 26
Organisms can grow rapidly in urine, so specimen must be transported immediately to the Lab. (Ideally the specimen should be examined within two hours of collection). The specimen should be refrigerated if it cannot be examined promptly or use boric acid (Bacteriostatic preservation).
07/30/26
Dr. Adnan Jaran
<number>

## Slide 27: Urine - Cathereized
Transport system: Sterile urine container
Volume : Same as for Urine
Catheterization is not
recommended for routine or
culture (Why?).
(Risk of inducing infection).
First portion is contaminated with urethral bacteria, so should be discarded ( similar to midstream-voided specimen).
Specimen must be transported rapidly to Lab.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 28: Urine – Suprapubic aspirate
Transport system: Sterile anaerobic tube or vial
Volume : Same as for Urine
This is an invasive specimen, so urethral bacteria are avoided.
Only valid method available for collecting specimens for anaerobic culture.
Also useful for collection of specimens from children or adults unable to void uncontaminated specimens.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 29: Diagnosis of UTI

## Slide 30: Mid Stream Specimen of Urine (MSSU)
Indications: Ideally the specimen should be examined within two hours of collection. The specimen should be refrigerated if it cannot be examined promptly or use boric acid.
Perform dipstick analysis first to detect leucocytes and nitrites. Leucocytosis (WBC) has 89 % sensitivity and 68 % specificity and nitrite has 57 of sensitivity and 96 % specificity.

## Slide 31: Specimen of Urine
Pregnancy : Dip sticks in early pregnancy may not always be enough to identify asymptomatic bacteriuria in pregnancy. Therefore MSSU specimen should be sent at the first antenatal visit.
Children : Low threshold for referral and investigation. Send urine sample for any sick child and every young child with unexplained fever.
Men: Suspected UTI as it is much less common than in women. Consider further investigation and referral.
Suspected pyelonephritis
Recurrent UTI may be caused by an antibiotic resistant organism

## Slide 32: Respiratory
Throat:
Transport system: Swab immersed in transport medium.
Area of inflammation is swabbed, contact with saliva should be avoided (Why?)
( inhibit the recovery of group A streptococci).
Epiglottis
Blood culture is done: as for blood culture.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 33: Respiratory
Sinuses
Transport system: Sterile anaerobic tube or vial.
Volume: 1 – 5 ml
Specimen must be collected with needle and syringe
Specimen should be cultured for aerobic and anaerobic bacteria.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 34: Respiratory
Lower airways
Transport system: Screw-capped bottle; anaerobic tube or vail.
Volume 1 -2 ml
Sputum is collected.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 35: Sputum
Indications: Sputum samples should be sent for culture and sensitivity from patients with pneumonia who are able to expectorate purulent samples and who have not received previous antibiotic therapy.
Not indicated: Specimens that are largely or wholly saliva yield misleading information and should not be sent for culture.
Specimen collection: The patient should be instructed to remove dentures, rinse mouth and gargle with tap water; not with antiseptic mouthwash. Early morning sample is preferred.

## Slide 37: Sputum
Specimen Transport:
Sputum specimens should be transported to the laboratory as quickly as possible. They should not be refrigerated

## Slide 38: Blood
Routine bacterial culture
Transport system: Blood culture bottle with nutrient media
Volume: - Adults: 20 ml/culture
        Children: 5-10 ml/culture
        Neonates: 1 – 2 ml/culture
Skin should be disinfected by 70% alcohol followed by 2% iodine.
2-3 cultures collected every 24hr, unless pt. is in septic shock.
07/30/26
Dr. Adnan Jaran
<number>

## Slide 39: Blood
Intracellular bacteria (Brucella, Francisella, Neisseria spp). Same as for routine culture
Leptospira spp. Use sterile heparinized tube volume 1 – 5 ml
07/30/26
Dr. Adnan Jaran
<number>

## Slide 40: Blood culture
Indications: Blood culture is recommended on all patients with suspected bacteraemia/ septicaemia.
Samples to send: Specimens must be collected using strict aseptic technique and before antibiotic treatment is commenced. No more than three specimens should be taken.
Other considerations: For patients with suspected endocarditis, three sets of blood culture in the first 24 hours (from separate venepunctures) are required. In an acutely ill patient, three sets of blood cultures should be taken within 2 hours before starting empirical therapy.

## Slide 41: Cerebrospinal fluid
Transport system: Sterile screw capped tube
Volume: Bacterial culture: 1 – 5 ml
      Mycobacterial culture as large a volume as possible
Other normally sterile fluids
(abdominal, chest, synovial, pericardial)
Sterile screw capped bottle or blood culture bottle for large volumes
Volume : as large as possiple
07/30/26
Dr. Adnan Jaran
<number>

## Slide 42: Stool for C. difficile
Indications: Only diarrohoeal stools (those that take the shape of the container) should be sent to the laboratory for the detection of C. difficile toxin.
Not indicated: Screening and treatment of asymptomatic patients is not necessary.
Frequency of Specimens: Once the diagnosis has been confirmed, repeat specimens for clearance need not be taken unless there is a relapse following treatment. This is because it is not uncommon for the faeces to remain toxin- positive for some time after the start of treatment, even when the patient’s symptoms have settled.

## Slide 43: Thank You
07/30/26
Dr. Adnan Jaran
<number>

## Slide 44
07/30/26
Dr. Adnan Jaran
<number>
Port-A-Cul anaerobic