## Slide 1: Chapter 13: Operational Amplifiers
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 2: Slide 1
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Basic Op-Amp
Operational amplifier or op-amp, is a very high gain differential amplifier with a high input impedance (typically a few mega ohms) and low output impedance (less than 100 ohms).
Note the op-amp has two inputs and one output.

## Slide 3: Slide 2
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Op-Amp Gain
Op-Amps have a very high gain. They can be connected open- or closed loop.
Open-loop refers to a configuration where there is no feedback from output back to the input. In the open-loop configuration the gain can exceed 10,000.
Closed-loop configuration reduces the gain. In order to control the gain of an op-amp it must have feedback. This feedback is a negative feedback. A negative feedback will reduce the gain and improve many characteristics of the op-amp.

## Slide 4: Slide 3
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Inverting Op-Amp
The input is applied to the inverting (-) input; the non-inverting input (+) is grounded. The resistor Rf is the feedback resistor; it is connected from the output to the negative (inverting) input. This is negative feedback.

## Slide 5: Slide 4
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Inverting Op-Amp Gain
Gain can be determined from external resistors: Rf and R1.
[Formula 13.8]
Unity Gain: Voltage gain is 1.
Rf = R1
[Insert Formula]
The negative sign denotes a 180 degree phase shift between input and output.
Constant Gain: Rf is a multiple of R1.
Voltage gain

## Slide 6: Slide 5
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Virtual Ground
An understanding of the concept of virtual ground provides a better understanding of how an op-amp operates.
The non-inverting input pin is at ground. The inverting input pin is also at 0V for an AC signal.
This is because the op-amp has such high input impedance that even with a high gain there is no current from inverting input pin, therefore there is no voltage from inverting pin to ground. All of the current is through Rf.
The AC equivalent circuit.

## Slide 7: Slide 6
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Practical Op-Amp Circuits
These Op-amp circuits are commonly used:
  Inverting Amplifier
  Noninverting Amplifier
  Unity Follower
  Summing Amplifier
  Integrator
  Differentiator

## Slide 8: Slide 7
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Inverting Op-Amp

## Slide 9: Slide 8
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Noninverting Amplifier
Notice the output formula is similar to Inverting Amplifier, but they are not the same.

## Slide 10: Slide 9
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Unity Follower
because Rf = R1
[Formula 13.10]

## Slide 11: Slide 10
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Summing Amplifier
Because the op-amp has a high input impedance the multiple inputs are treated as separate inputs.
[Formula 13.11]

## Slide 12: Slide 11
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Integrator
The output is the integral of the input. Integration is the operation of summing the area under a waveform or curve over a period of time. This circuit is useful in low-pass filter circuits and sensor conditioning circuits.
[Formula 13.13]

## Slide 13: Slide 12
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Differentiator
The differentiator takes the derivative of the input. This circuit is useful in high-pass filter circuits.
[Formula 13.15]

## Slide 14: Slide 13
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Op-Amp Specifications – DC Offset Parameters
Even though the input voltage is 0, there will be an output. This is called offset. The following can cause this offset:
  Input Offset Voltage
  Output Offset Voltage due to Input Offset Current
  Total Offset Voltage Due to Input Offset Voltage and Input Offset Current
  Input Bias Current

## Slide 15: Slide 14
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Input Offset Voltage (VIO)
The specification sheet for an op-amp will indicate an input offset voltage (VIO).
The effect of this input offset voltage on the output can be calculated:
[Formula 13.16]

## Slide 16: Slide 15
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Output Offset Voltage due to Input Offset Current (IIO)
If there is a difference between the dc bias currents for the same applied input, then this too will cause an output offset voltage:
The Input Offset Current (IIO) is specified in the specifications for the op-amp.
The effect on the output can be calculated:
[Formula 13.16]

## Slide 17: Slide 16
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Total Offset due to VIO and IIO
The op-amp may have an output offset voltage due to both factors VIO and IIO. The total output offset voltage will be the sum of the effects of both:
[Formula 13.19]
Vo(offset) = Vo(offset due to VIO) + Vo(offset due to IIO)

## Slide 18: Slide 17
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Input Bias Current (IIB)
A parameter that is related to Input Offset Current (IIO) is called Input Bias Current (IIB).
The separate Input Bias Currents are:
The total Input Bias Current is the average:
[Formula 13.21]
[Formula 13.20]

## Slide 19: Slide 18
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Op-Amp Specifications – Frequency Parameters
An op-amp is a wide-bandwidth amplifier. The following affect the bandwidth of the op-amp.
  Gain
  Slew Rate

## Slide 20: Slide 19
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Gain and Bandwidth
The op-amp’s high frequency response is limited by internal circuitry. The plot shown is for an open loop gain (AOL or AVD). This means that the op-amp is operating at the highest possible gain with no feedback resistor.
In the open loop, the op-amp has a narrow bandwidth.
The bandwidth will widen in closed loop operation, but then the gain will be lower.

## Slide 21: Slide 20
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Slew Rate (SR)
Slew rate is the maximum rate at which an op-amp can change output without distortion.
The SR rating is given in the specification sheets as V/s rating.
[Formula 13.23]
V/s

## Slide 22: Slide 21
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Maximum Signal Frequency
The slew rate determines the highest frequency of the op-amp without distortion.
where VP is the peak voltage

## Slide 23: Slide 22
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
General Op-Amp Specifications
Other ratings for op-amp found on specification sheets are:
Absolute Ratings
Electrical Characteristics
Performance

## Slide 24: Slide 23
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Absolute Ratings
These are commonly the maximum ratings for the op-amp.

## Slide 25: Slide 24
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Electrical Characteristics
Note these ratings are for specific circuit conditions, and they often include minimum, maximum and typical values.

## Slide 26: Slide 25
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
CMRR
One rating worth mentioning that is unique to op-amps is CMRR or Common-Mode Rejection Ratio.
Because the op-amp has two inputs that are opposite in phase (inverting input and the non-inverting input) any signal that is common to both inputs will be cancelled.
A measure of the ability to cancel out common signals is called CMRR.

## Slide 27: Slide 26
Robert Boylestad Digital Electronics
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.
Op-Amp Performance
The specification sheets will also include graphs that indicate the performance of the op-amp over a wide range of conditions.